# Standard Deviation for SST Reynolds error.
22-01-2007
Sophie RICCI
CERFACS
------------------------------------------------------------------------------------------------------------------
The purpose is to enable the use of a 2d map for the standard deviation on the SST error instead
 of a constant value.
------------------------------------------------------------------------------------------------------------------
### Build the 2d map for the observation error using Reynolds SST
The (normalized) variance for the error is provided weekly by ncep along with the SST files. ftp://ftp.emc.ncep.noaa.gov/cmb/sst/oisst_v2/
This error is mostly due to the objective analysis error as well as the measurement error on the SST.

A temporal mean for this variance is computed over 1993-2003 using an IDL routine.
read_ncep_sstreynolds.pro
SST and variance are read in the original weekly binary files and a temporal mean is computed.
The mask is read in lstags.onedeg.dat
The ocean and land point convention needs to be reversed to match the ORCA convention.
The mask and longitude arrays need to be shifted in order to match the data array. There seems to be an error in the NCEP README file: the data start at -9.5 E (350.5) instead of 0.5 E.
The variance is multiplied by the mask.
Mean_sst, mean_err, mask, lon,lat are writen in a binary file
home/ms/spfroasp/lmr/SST_REYNOLDS/sst_reynolds_meansst_meanvariance_1993_2003'

### Interpolation to ORCA grid using OASIS
See hpce0105{/home/ms/spfroasp/lmr/Interpolations_to_orca}
and hpce0105{/tmp/ms/spfroasp/lmr/Interpolations_to_orca} . This is the working directory where the script should be executed.

Files to provide:
interpolation files:
areas.nc
tmasks.nc
tmasks_grids.nc
namcouple_ncep
cf_name_table.txt
executable:
oasis*
input file:
mean_normalized_std_dev_ncep_interpolatedto_orca.nc
script:
interp_ncep.ksh

IDL routine write_input_interpolationtoorca.pro writes to .nc files
tmask_ncep.nc
tmasks_grids_ncep.nc
areas.nc
It also writes the input file (mean_variance and mean_std_dev in mean_normalized_std_dev_ncep_interpolatedto_orca.nc)

A few modifications:

The .nc files are written using ncdf_quickwrite from SAXO package.
(http://forge.ipsl.jussieu.fr/saxo/download/idldoc_html_output/index.html)

The longitude and latitude variables in these files need to be renamed:
ncrename -v ncep_mask, ncep.msk tmask_ncep.nc
ncrename ncep_lon, ncep.lon ncep_lat,ncep.lat tmasks_grids_ncep.nc
ncrename areas,ncep.srf areas_ncep.nc

The variable ncep.msk needs to be INT instead of SHORT:
ncap -s ncep.msk2=int(ncep.msk) tmasks_ncep.nc
ncrename -v ncep.msk2,ncep.msk tmasks_ncep.nc
or
ncdump file.nc > tempfile
vi tempfile , modify tempfile
ncgen -o tempfile.nc tempfile

The output file is out.nc in /hpce/tmp/ms/spfroasp/lmr/Interpolations_to_orca/WORK
In order to use IONCDF package in OPAVAR, the dimension time counter must be removed :
ncwa -1 time_counter toto.nc tata.nc

The std dev must be a DOUBLE precision variable:
ncap -O -h -v -s “std_dev_ncep=double(std_dev_ncep” tata.nc titi.nc

Script:

This file must be copied under ecfs and read in by getjop (osddir)
Add DRIOSD=/$OCSSETUP/$OPA_GRID/ERRORS to opavar.h
(ec:/ocx/OPAVAR/SETUP/ORCA2/ERROBS/err_obs_sst_reynolds.nc)
In the code: obsesd.F

The general name file is err_obs_sst_reynolds.nc, the variable name is std_dev_ncep.
call get_var(cl_filenamesst,cl_varsst, z_varsst,z_missing) in obsesd.F
A flag NSDSSTP is added in namelist.var (0: constante value / 1: gridded field read in from file), common.var.h, and prepifs ADDITIONAL VARIABLES, and set to 1.
(To use the relan procedure, the variable must be added to job_orcavar_param)